## Slide 1
Indigenous AI Compute Engine
01 / 11
Indigenous AI Accelerator
Design & Development
A programmable FPGA compute platform
with a roadmap for more models and operators.
ARCHITECTURE
BUILD RESULTS
CURRENT STATUS
8 × 32
SYSTOLIC COMPUTE FABRIC
INT8 / INT16 · MICROCODE CONTROL
• RTL architecture • memory hierarchy • FPGA integration
Notes: PRESENTER SPEECH
This presentation introduces the design and development of our Unified C-Engine AI accelerator on the AMD ZCU106. The aim is to build a programmable compute platform that can grow over time. Four model integrations are available today: MNIST LeNet-5, ResNet-50, MobileNetV2 and EfficientNet-B0. More models and operators will follow as the compiler and RTL evolve. I will explain the system and engine architecture, the memory hierarchy, and the software flow, then show the implementation evidence and the remaining development milestones. The results are drawn from saved repository artifacts, so each performance claim is tied to its recorded scope.
TECHNICAL REFERENCES AND QUALIFICATIONS
Scope: a concise project overview based on files in E:/unified, reviewed 2026-10-19. No new FPGA build, simulation, or board execution was performed for this presentation. Raw routed reports and saved execution logs take precedence over summary prose when numbers disagree. Some logs reference source snapshots outside the current checkout; they are recorded results, not a fresh verification of the present files.

## Slide 2
COMPILER + RUNTIME: The software makes the hardware reusable
Compilation generates the data and instruction stream for each model; deployment launches the same engine.
02 / 11
Import
Load PyTorch parameters
and model structure
01
Transform
Fold BatchNorm; quantize
weights and activations
02
Schedule
Tile tensors; assign SRAM
rows and layer controls
03
Emit
Weights, 128-bit microcode,
stimulus and metadata
04
JTAG / XSDB preload weights in DDR
ARM + AXI-Lite launch
DDR logits → UART
Indigenous AI Compute Engine
Notes: PRESENTER SPEECH
At the system level, the ARM processor manages the inference job. It prepares configuration, launches transfers and presents the returned predictions. The FPGA programmable logic executes the scheduled neural compute. Images and weights begin in DDR, move through the DMA read path into banked SRAM, and feed the compute array. Post-processing transforms the accumulated results before they return to SRAM. The write DMA then returns the final logits to DDR. Microcode coordinates the layer sequence. This separation provides a reusable accelerator architecture while keeping control and result handling in a familiar baremetal software environment.
TECHNICAL REFERENCES AND QUALIFICATIONS
Sources: rtl/c_engine_dma_top.v, rtl/c_engine_top.v, rtl/axi_lite_slave.v, rtl/axi4_master_rd.v, rtl/axi4_master_wr.v, rtl/dma_sram_bridge.v, baremetal/src/c_engine_driver.c and main.c. Diagram is a functional overview; controller signals and SRAM return paths are summarized in the data-path caption. PPU means post-processing unit. Main CPU also performs softmax and top-k result presentation, so the broad README phrase "zero neural network math" is not repeated.

## Slide 3
SYSTEM ARCHITECTURE
From Python Model assets to FPGA inference
The processing system controls the overall inference run; the programmable logic performs the scheduled compute involved in four models
Indigenous AI Compute Engine
03 / 11
PROCESSING SYSTEM
ARM Cortex-A53
Baremetal driver + AXI-Lite
PS DDR4
Images, weights, microcode
Using JTAG
PROGRAMMABLE LOGIC
AXI-Lite
Registers + status
Microcode sequencer
Layer control, address generation and DMA triggers
128-bit DMA
Read + write masters
Banked SRAM
Activations + weights
256 PEs + PPU
MAC, activation, pooling
Data path: DDR → SRAM → compute / post-processing → SRAM → DDR
Notes: PRESENTER SPEECH
At the system level, the ARM processor manages the inference job. It prepares configuration, launches transfers and presents the returned predictions. The FPGA programmable logic executes the scheduled neural compute. Images and weights begin in DDR, move through the DMA read path into banked SRAM, and feed the compute array. Post-processing transforms the accumulated results before they return to SRAM. The write DMA then returns the final logits to DDR. Microcode coordinates the layer sequence. This separation provides a reusable accelerator architecture while keeping control and result handling in a familiar baremetal software environment.
TECHNICAL REFERENCES AND QUALIFICATIONS
Sources: rtl/c_engine_dma_top.v, rtl/c_engine_top.v, rtl/axi_lite_slave.v, rtl/axi4_master_rd.v, rtl/axi4_master_wr.v, rtl/dma_sram_bridge.v, baremetal/src/c_engine_driver.c and main.c. Diagram is a functional overview; controller signals and SRAM return paths are summarized in the data-path caption. PPU means post-processing unit. Main CPU also performs softmax and top-k result presentation, so the broad README phrase "zero neural network math" is not repeated.

## Slide 4
FPGA SYSTEM INTEGRATION
FPGA implementation: the PS–PL Interface
Vivado block-design connections for the accelerator IP on the Zynq UltraScale+ MPSoC.
04 / 11
PROCESSING SYSTEM (PS)
PROGRAMMABLE LOGIC (PL)
ARM / M_AXI_HPM0_FPD
Control master: 128-bit AXI
PS DDR / S_AXI_HP0_FPD
Read-data return: 128 bits
PS DDR / S_AXI_HP1_FPD
Write-data destination: 128 bits
axi_smc_ctrl
128 → 32-bit control
axi_smc_rd
Read SmartConnect
axi_smc_wr
Write SmartConnect
Compute engine
s_axi_lite / register control
m0_axi / read DMA master
m1_axi / write DMA master
Arrows show control / payload flow; DMA requests originate in PL.
pl_clk0 → shared clock
rst_ps8_0 → resets
interrupt → PS pl_ps_irq0
Indigenous AI Compute Engine
Notes: PRESENTER SPEECH
This diagram maps the accelerator onto the actual Vivado system connections. At the top, the ARM processing system sends configuration through its HPM master port and a control SmartConnect to the accelerator's AXI-Lite interface. The accelerator has separate read and write DMA masters. Read data returns from DDR through HP0, while output data travels through HP1 on the write path. The arrows here show payload movement; the DMA requests themselves originate in the FPGA logic. The design shares the PS-generated PL clock, uses the processor-system reset block, and connects the accelerator interrupt back to the PS. These interfaces form the system-level contract for future accelerator extensions.
TECHNICAL REFERENCES AND QUALIFICATIONS
Primary source: fpga/create_bd.tcl executable commands. PS M_AXI_HPM0_FPD connects via axi_smc_ctrl to s_axi_lite; m0_axi connects via axi_smc_rd to S_AXI_HP0_FPD; m1_axi via axi_smc_wr to S_AXI_HP1_FPD. The diagram arrows show control writes and payload movement, not AXI master/slave transaction direction. The DMA masters are in PL. Control address aperture is 0xA0000000–0xA000FFFF. Both DMA address spaces map a 2 GiB DDR-low aperture, 0x00000000–0x7FFFFFFF; this is distinct from the board physical DDR capacity. pl_clk0 drives accelerator, interconnects, PS AXI clocks and reset synchronizer. pl_resetn0 feeds rst_ps8_0; peripheral_aresetn resets accelerator and SmartConnects. Accelerator interrupt connects to pl_ps_irq0. Some file comments refer to ZCU104 or 125 MHz; the executable default is ZCU106 and 75 MHz. No new implementation run was made.

## Slide 5
RTL MODULE ARCHITECTURE
RTL engine architecture: modules and data paths
The DMA wrapper handles transfers; the compute core contains instruction memory, SRAM, control and the PE array.
05 / 11
PL Implementation Architecture
axi_lite_slave
Control / status / config
axi4_master_rd / wr
128-bit read / write AXI
dma_sram_bridge
128-bit beat → SRAM bank
config_mem
256 × 128 bits
c_engine_controller
FSM + GAP
Requantization PPU
multibank_dualport_mem
Port A: DMA / controller mux; Port B: compute
compute_engine
8 × 32 processing_element
Requantized writeback
Solid: data / instructions · Dashed: array control · PPU is instantiated inside the controller
Indigenous AI Compute Engine
Notes: PRESENTER SPEECH
Here we move inside the RTL hierarchy. The outer DMA wrapper contains the AXI-Lite register interface, the read and write masters, and the bridge that maps transfer beats into SRAM banks. Inside the compute core, configuration memory feeds the sequencer. The controller selects operands and controls the processing-element array. Array results pass through the requantization and post-processing unit, which is instantiated inside the controller, before returning to SRAM. Port A is shared through a DMA-versus-controller multiplexer, while Port B serves the compute path. This modular boundary helps us identify what changes when adding an operator: its scheduling, operand steering, arithmetic or post-processing requirements.
TECHNICAL REFERENCES AND QUALIFICATIONS
Sources: rtl/c_engine_dma_top.v instantiates u_axi_lite, u_master_rd, u_master_wr, u_bridge and u_engine. rtl/c_engine_top.v instantiates u_memory, u_config_mem, u_controller and u_c_engine. Port A is selected by ext_mem_override between bridge/host and controller; Port B is controller-driven. c_engine_controller.v assigns engdata_in from mem_dout_b; GEMV weights come from mem_dout_a, convolution uses its staged weight table; PPU requantization_block instance u_requant belongs to the controller. The diagram summarizes operand paths through controller steering rather than drawing every mux and bus. PPU receives PE results plus residual data and writes back under controller control. GAP reduction is also inside the controller. The dashed arrow shows PE enable and steering controls; additional controller SRAM and DMA handshakes are omitted for legibility. Config words are 128 bits according to active headers despite legacy comments saying 96 bits.

## Slide 6
COMPUTE DESIGN
Inside the compute engine
One parameterized grid supports convolution, depthwise execution and dense matrix-vector stages.
06 / 11
256 signed MAC units
Horizontal / vertical forwarding
Local accumulation + bias injection
01
Accumulate
INT8 → INT32; INT16 → INT48
02
Requantize
Arithmetic shift and saturation
03
Fuse
Residual add + ReLU / Leaky ReLU / LUT
04
Write back
Stride, pooling and registered SRAM output
38.4 GOP/s theoretical INT8 peak at 75 MHz
Indigenous AI Compute Engine
Notes: PRESENTER SPEECH
Here we move inside the RTL hierarchy. The outer DMA wrapper contains the AXI-Lite register interface, the read and write masters, and the bridge that maps transfer beats into SRAM banks. Inside the compute core, configuration memory feeds the sequencer. The controller selects operands and controls the processing-element array. Array results pass through the requantization and post-processing unit, which is instantiated inside the controller, before returning to SRAM. Port A is shared through a DMA-versus-controller multiplexer, while Port B serves the compute path. This modular boundary helps us identify what changes when adding an operator: its scheduling, operand steering, arithmetic or post-processing requirements.
TECHNICAL REFERENCES AND QUALIFICATIONS
Sources: rtl/c_engine_dma_top.v instantiates u_axi_lite, u_master_rd, u_master_wr, u_bridge and u_engine. rtl/c_engine_top.v instantiates u_memory, u_config_mem, u_controller and u_c_engine. Port A is selected by ext_mem_override between bridge/host and controller; Port B is controller-driven. c_engine_controller.v assigns engdata_in from mem_dout_b; GEMV weights come from mem_dout_a, convolution uses its staged weight table; PPU requantization_block instance u_requant belongs to the controller. The diagram summarizes operand paths through controller steering rather than drawing every mux and bus. PPU receives PE results plus residual data and writes back under controller control. GAP reduction is also inside the controller. The dashed arrow shows PE enable and steering controls; additional controller SRAM and DMA handshakes are omitted for legibility. Config words are 128 bits according to active headers despite legacy comments saying 96 bits.

## Slide 7
Overall MEMORY HIERARCHY
Memory hierarchy: DDR capacity to PE-local reuse
Explicitly managed storage keeps bulk model data off chip and active compute data close to the array.
07 / 11
PS DDR4 — images, weights and output logits
Large external store; DMA sees the mapped 2 GiB DDR-low aperture
128-bit AXI bursts / 16 bytes per beat
Banked on-chip SRAM — active tensors and weights
INT8: 3.93 MB, 256 B/row | INT16: 2.10 MB, 512 B/row
Controller selects rows, banks and operands
Weight staging + GAP / output registers
PE registers: HOR / VERT / ENG / Outf_map
CONTROL STORAGE
config_mem: 4 KiB
256 instructions × 128 bits
AXI-Lite programming → sequencer
DDR ADDRESS EXAMPLE
0x20100000 ImageNet input
0x21000000 Microcode assets
0x31000000 ResNet-50 weights
0x38000000 Output logits
Read path shown; results return through SRAM and write DMA to DDR.
Indigenous AI Compute Engine
Notes: PRESENTER SPEECH
Here we move inside the RTL hierarchy. The outer DMA wrapper contains the AXI-Lite register interface, the read and write masters, and the bridge that maps transfer beats into SRAM banks. Inside the compute core, configuration memory feeds the sequencer. The controller selects operands and controls the processing-element array. Array results pass through the requantization and post-processing unit, which is instantiated inside the controller, before returning to SRAM. Port A is shared through a DMA-versus-controller multiplexer, while Port B serves the compute path. This modular boundary helps us identify what changes when adding an operator: its scheduling, operand steering, arithmetic or post-processing requirements.
TECHNICAL REFERENCES AND QUALIFICATIONS
Sources: rtl/c_engine_dma_top.v instantiates u_axi_lite, u_master_rd, u_master_wr, u_bridge and u_engine. rtl/c_engine_top.v instantiates u_memory, u_config_mem, u_controller and u_c_engine. Port A is selected by ext_mem_override between bridge/host and controller; Port B is controller-driven. c_engine_controller.v assigns engdata_in from mem_dout_b; GEMV weights come from mem_dout_a, convolution uses its staged weight table; PPU requantization_block instance u_requant belongs to the controller. The diagram summarizes operand paths through controller steering rather than drawing every mux and bus. PPU receives PE results plus residual data and writes back under controller control. GAP reduction is also inside the controller. The dashed arrow shows PE enable and steering controls; additional controller SRAM and DMA handshakes are omitted for legibility. Config words are 128 bits according to active headers despite legacy comments saying 96 bits.

## Slide 8
MEMORY + PRECISION
SRAM Memory planning is central to scaling
DDR stores large model assets; banked SRAM stages the active tensors and weight tiles.
08 / 11
CONFIGURATION
INT8 BUILD
INT16 BUILD
Arithmetic
8-bit inputs / weights; 32-bit sums
16-bit inputs / weights; 48-bit sums
SRAM geometry
16 banks × 128 bits × 15,360 rows
32 banks × 128 bits × 4,096 rows
Logical capacity
3.93 MB (3.75 MiB)
2.10 MB (2.00 MiB)
Instruction store
256 × 128-bit words
256 × 128-bit words
Example: current ResNet-50 INT8 compiler allocation of SRAM rows
Input +
stage 0
Ping
Pong
Residual
Weights
Indigenous AI Compute Engine
Notes: PRESENTER SPEECH
Here we move inside the RTL hierarchy. The outer DMA wrapper contains the AXI-Lite register interface, the read and write masters, and the bridge that maps transfer beats into SRAM banks. Inside the compute core, configuration memory feeds the sequencer. The controller selects operands and controls the processing-element array. Array results pass through the requantization and post-processing unit, which is instantiated inside the controller, before returning to SRAM. Port A is shared through a DMA-versus-controller multiplexer, while Port B serves the compute path. This modular boundary helps us identify what changes when adding an operator: its scheduling, operand steering, arithmetic or post-processing requirements.
TECHNICAL REFERENCES AND QUALIFICATIONS
Sources: rtl/c_engine_dma_top.v instantiates u_axi_lite, u_master_rd, u_master_wr, u_bridge and u_engine. rtl/c_engine_top.v instantiates u_memory, u_config_mem, u_controller and u_c_engine. Port A is selected by ext_mem_override between bridge/host and controller; Port B is controller-driven. c_engine_controller.v assigns engdata_in from mem_dout_b; GEMV weights come from mem_dout_a, convolution uses its staged weight table; PPU requantization_block instance u_requant belongs to the controller. The diagram summarizes operand paths through controller steering rather than drawing every mux and bus. PPU receives PE results plus residual data and writes back under controller control. GAP reduction is also inside the controller. The dashed arrow shows PE enable and steering controls; additional controller SRAM and DMA handshakes are omitted for legibility. Config words are 128 bits according to active headers despite legacy comments saying 96 bits.

## Slide 9
An AI accelerator platform with four model integrations
Current model support spans digit recognition and ImageNet vision workloads; validation maturity varies by model.
Indigenous AI Compute Engine
09 / 11
256
processing elements
4
model compiler flows
2
precision builds
1,000
ImageNet output classes
MNIST / LeNet-5
Digit recognition
10 classes
5 microcode words
ResNet-50
Residual network
1,000 classes
57 microcode words
MobileNetV2
Depthwise convolution
1,000 classes
56 microcode words
EfficientNet-B0
MBConv + Swish LUT
1,000 classes
53 microcode words
Platform direction: The model and operator coverage can be expanded using python compiler, reusable RTL and systematic validation.
Notes: PRESENTER SPEECH
At the system level, the ARM processor manages the inference job. It prepares configuration, launches transfers and presents the returned predictions. The FPGA programmable logic executes the scheduled neural compute. Images and weights begin in DDR, move through the DMA read path into banked SRAM, and feed the compute array. Post-processing transforms the accumulated results before they return to SRAM. The write DMA then returns the final logits to DDR. Microcode coordinates the layer sequence. This separation provides a reusable accelerator architecture while keeping control and result handling in a familiar baremetal software environment.
TECHNICAL REFERENCES AND QUALIFICATIONS
Sources: rtl/c_engine_dma_top.v, rtl/c_engine_top.v, rtl/axi_lite_slave.v, rtl/axi4_master_rd.v, rtl/axi4_master_wr.v, rtl/dma_sram_bridge.v, baremetal/src/c_engine_driver.c and main.c. Diagram is a functional overview; controller signals and SRAM return paths are summarized in the data-path caption. PPU means post-processing unit. Main CPU also performs softmax and top-k result presentation, so the broad README phrase "zero neural network math" is not repeated.

## Slide 10
RECORDED RESULTS
Recorded Results (Full end to end): Int8
Saved INT8 logs show functional completion; elapsed hardware time below is calculated from cycles at 75 MHz.
10 / 11
MODEL / Input Image
CYCLES
TIME AT 75 MHz
RECORDED OUTCOME
MNIST / raw 8 × 32 MNIST input
350
4.66 µs
PASS (0/10 mismatches)
MobileNetV2 / full RGB 224x224x3
3,047,626
40.63 msec
PASS (0 / 1,000 mismatches)
EfficientNet-B0 / full RGB 224x224x3
3,795,311
50.6 msec
PASS (0 / 1,000 mismatches)
ResNet-50 / full RGB 224x224x3
76,275,902
1017 msec
PASS (0/1,000 mismatches) –In progress
24.6 FPS / MobileNetV2
19.7 FPS / EfficientNet-B0
Indigenous AI Compute Engine
Notes: PRESENTER SPEECH
Here we move inside the RTL hierarchy. The outer DMA wrapper contains the AXI-Lite register interface, the read and write masters, and the bridge that maps transfer beats into SRAM banks. Inside the compute core, configuration memory feeds the sequencer. The controller selects operands and controls the processing-element array. Array results pass through the requantization and post-processing unit, which is instantiated inside the controller, before returning to SRAM. Port A is shared through a DMA-versus-controller multiplexer, while Port B serves the compute path. This modular boundary helps us identify what changes when adding an operator: its scheduling, operand steering, arithmetic or post-processing requirements.
TECHNICAL REFERENCES AND QUALIFICATIONS
Sources: rtl/c_engine_dma_top.v instantiates u_axi_lite, u_master_rd, u_master_wr, u_bridge and u_engine. rtl/c_engine_top.v instantiates u_memory, u_config_mem, u_controller and u_c_engine. Port A is selected by ext_mem_override between bridge/host and controller; Port B is controller-driven. c_engine_controller.v assigns engdata_in from mem_dout_b; GEMV weights come from mem_dout_a, convolution uses its staged weight table; PPU requantization_block instance u_requant belongs to the controller. The diagram summarizes operand paths through controller steering rather than drawing every mux and bus. PPU receives PE results plus residual data and writes back under controller control. GAP reduction is also inside the controller. The dashed arrow shows PE enable and steering controls; additional controller SRAM and DMA handshakes are omitted for legibility. Config words are 128 bits according to active headers despite legacy comments saying 96 bits.

## Slide 11
RESULT INTERPRETATION
A correct top-1 example is only part of accuracy
The saved dog-image runs identify Samoyed, while the full distributions reveal quantization limits.
11 / 11
TEST IMAGE: DOG.JPG
MobileNetV2: Samoyed #258
Logit 90; next recorded class is thunder snake (72).
EfficientNet-B0: three-way top tie
Samoyed, ibex and analog clock all saturate at 127.
What the evidence supports
Exact agreement with the logged quantized reference.
A limited sample; held-out dataset accuracy remains open.
Indigenous AI Compute Engine
Notes: PRESENTER SPEECH
This example helps explain why we look beyond the pass marker. The dog-image runs report Samoyed as top one. MobileNetV2 has a clear highest logit in this capture. EfficientNet-B0, however, gives three classes the maximum INT8 value of 127, so its top result includes a saturation tie. Agreement with a quantized reference is valuable evidence about execution, but it does not establish general classification accuracy. We need to examine output distributions, fix saturation where appropriate, and evaluate on images that were not used for calibration. That becomes more important as we bring additional models onto the accelerator.
TECHNICAL REFERENCES AND QUALIFICATIONS
Sources: data/test_images/dog.jpg; sim/logs/mobilenetv2_8bit.log, efficientnetb0_8bit.log. MobileNet Top-5 = [258:90,52:72,904:56,0:53,61:53]. EfficientNet Top-5 = [258:127,350:127,409:127,128:117,146:116]; the tie at INT8 maximum limits interpretation of a top1=258 marker. Zero mismatches means agreement with the logged fixed-point reference, not proof of equivalence to floating-point PyTorch on all images. The current compiler explicitly calibrates a projected head using test-image features. No held-out benchmark accuracy result was located in the reviewed project evidence. This slide intentionally avoids the V4 prose claim of 100% PyTorch bit-exact accuracy.